Addendum B

2011 Design Quality Standards

(For Single-Family Homes)

The following outline of minimum standards must be used in designing Housing Credit and HOME projects of twelve or more units and consist of single-family.  All single-family homes must be new construction.

Any deviations from these standards should have the prior written consent or approval of the Alabama Housing Finance Authority fourteen (14) days prior to submitting an application for funding.  Any deviation requested and approved less than fourteen (14) days prior to submitting an application will be charged $500.

Any deviations from these standards after the reservation for funding and through the construction of the project should have the prior written consent or approval of Alabama Housing Finance Authority before the work has commenced.  Any deviation requested and approved will be charged $500.

All projects must be designed in accordance with the applicable requirements of the Americans with Disabilities Act, Section 504 Requirements, Fair Housing and any local building codes.

I.	Site Selection Criteria:

HOME proposed sites containing property within a 100-year flood plain and/or wetlands are not permitted.

Sites located in a Radon Zone-1 (highest level) will require Radon Resistant New Construction Practices.  The following counties are located in Radon Zone-1:  Calhoun, Clay, Cleburne, Colbert, Coosa, Franklin, Jackson, Jefferson, Lauderdale, Lawrence, Limestone, Madison, Morgan, Shelby, and Talladega.

All developments must submit a complete site specific soils report, not more than one year old at the time of submission of final plans and specifications, bound within the project specifications.  The soils report must reflect the results of laboratory tests conducted on a minimum of one (1) soil boring for every two (2) single family buildings and a minimum total of two (2) soil borings at the planned paved areas of the development.  A registered professional engineer or a certified testing agency with a current license to practice in the State of Alabama must prepare the report.

Sites located outside municipal city limits:

1.	A proposed new construction site may be located outside a municipality’s city limit, but must be within the local police or sheriff jurisdiction.

2.	A proposed site that is located in the police jurisdiction of a local municipality must comply with applicable zoning restrictions as if located within that municipality’s city limit.

3.	Domestic water and fire water service must be provided to the development by the local utility service provider.

II.	Building Design Criteria

A.	Maximum Building Standards:

1.	The square footage of the Project’s community building must not exceed 2,500 square feet heated and cooled (inclusive of the office area, community laundry, community meeting room, mechanical room, restrooms, kitchens, etc.) and be ADA accessible.

2.	All 100% Elderly projects must be one-story structures.

B.	Minimum Building Standards:

1.	Minimum Unit Net Area Requirements:

“Net” area is measured from the interior finished face of the exterior wall to the centerline of the common, or party, wall.

Minimum Bedroom Net Area is measured from the interior faces of all walls surrounding each bedroom, excluding closets, mechanical rooms, and storage rooms.

| Unit Type | Number of Bathrooms | Minimum Unit Net Area* | Min. Bedroom Net Area |
| --- | --- | --- | --- |
| 3 Bedroom | 2 | 1,200 s.f. | 120 s.f. |
| 4 Bedroom | 2 | 1,455 s.f. | 120 s.f. |

*Note 1: Unit areas do not include outside storage, covered porches, patios, balconies, etc.

2.	All units must include an exterior storage closet with a minimum area of sixteen (16) square feet.

3.	All single-family rental homes must have a minimum of thirty (30) feet of building facing the front street.  This thirty (30) feet must be the sum of all front-facing dimensions adjacent to conditioned space and can include the “common” wall which is part of a front-facing garage as long as this wall is front-facing and conditioned on one side.

4.	All single-family rental homes must have a minimum of thirty (30) feet front yard building set-back from the curb.  Each home must have a minimum of ten (10) foot side yards.  (Minimum width of lot shall be fifty (50) feet.)  Both lot width and side yard setbacks can be modified with the following exception:  A ten (10) foot side yard setback on one lot side and a “zero lot line” setback on the other (thus, a forty (40) foot minimum lot width) will be allowed with a front-facing garage.

5.	All single-family rental homes must have a minimum of three (3) different front and rear elevation designs.  No identical front elevations may be built next to each other.

6.	All single-family rental homes must have a minimum of three (3) different color schemes.

7.	Exterior Building Standards:

a.	Exterior Finishing Materials:

1.	Exterior building coverings:  Very low maintenance materials are required. Acceptable materials include:

a.	Brick;

b.	High quality vinyl siding with a minimum thickness of .042 and a lifetime non-prorated limited warranty (50 year) transferable; or

c.	Cementitious siding.

All siding materials listed above are required to be 8 inches above the finished floor elevation of the building ground floor, with the exception of concrete patio and covered breezeway areas.  Brick or decorative block must be used as an apron material.

2.	Prefinished fascia and soffit: Vinyl, aluminum, and/or perforated cementitious panels should be used and must contain vents.

3.	Windows frames and sashes are to be constructed of vinyl-clad wood, solid extruded vinyl, fiberglass, or aluminum and all windows are required to have screens.

4.	Materials for entry doors are to be metal-clad wood, fiberglass, or hollow metal 	construction.  “Peepholes” and deadbolt locks are required in entry doors.  Dead bolt locks on entry doors should have “thumb latch” on interior side.  Double keyed dead bolt locks are prohibited.  Minimum clear width of all exterior doors shall be 34 inches.

5.	Roofing materials: Anti-fungal shingles or metal roof with 25-year warranty or better should be used.

6.	Roof gable vents should be made of aluminum or vinyl materials.  All roof penetrations must be located on the rear most section of the roofline.

7.	All attics shall be vented.

8.	Exterior shutters are required on all single-family homes.

9.	Units where a conventional wood frame foundation system is used, a non-wood “maintenance-free” composite decking material may be used at porches above a pressure treated wood framing system.

b.	Other Exterior Standards:

1.	Exterior lighting is required at entry doors.

2.	Address numbers are to be clearly visible.

3.	Two parking spaces for each home.

4.	Metal flashing or 20 mil polyethylene when used in conjunction with self-adhering 	polyethylene laminate flashing, should be installed above all exterior door and window units.

5.	A landscaping plan must be submitted indicating areas to be sodded and landscaped. Landscaping plan(s) must follow any applicable landscape municipal ordinance.  At a minimum, all disturbed areas must be seeded.  All rental units must have minimum of two (2) trees per unit and twelve (12) 1 gallon shrubs per unit.

6.	Concrete curbing is required along all paved areas throughout the development site, 	including parking areas.  Six (6) inch raised curbs and gutter design is required.  No valley curbs allowed.

7.	Sidewalk access to the front door and the driveway must be provided.

8.	A project sign including the fair housing logo is required.

9.	A minimum of one enclosed on a minimum of 3 sides trash dumpster or compactor or individual dumpster at each home is required by the local unit of government.  If a trash dumpster/compactor is provided it must be ADA accessible.

10.	Continuous asphalt or concrete paved access road must be provided to the entrance of the development.

11.	All community parking must be asphalt or concrete.  An asphalt or concrete paving recommendation letter must be provided with the application by a geotechnical engineer.

12.	All sidewalks and walkways must be concrete and at least 36 inches wide.  All amenities should be connected to the dwelling units by a sidewalk or walkway on one side of the street throughout the development.

13.	All driveways must be concrete.

14.	Mailboxes, playground and all exterior project amenities must be ADA accessible.

8.	Interior Building and Space Standards:

a.	Wall Framing:

1.	Walls may be framed using metal studs in lieu of wood.

2.	Sound proofing or sound batt insulation is required between the stud framing in party walls.  A sound rating of STC 54 is required.

b.	Insulation Requirements:

1.	Exterior wall insulation should have an overall R-11 minimum for the entire wall assembly.

2.	Roof or attic insulation should have an R-30 minimum.

3.	Vapor retarders must be installed if recommended by project architect.

Kitchen spaces:

1.	6 1/2-inch deep double bowl stainless steel sinks are required in each unit.

2.	Each unit must be equipped with a 5 lb. ABC rated dry chemical fire extinguisher 	readily accessible in the kitchen and mounted to accommodate handicapped accessible height in accessible units.

3.	New cabinets should have dual sidetrack drawers and no laminate or particleboard fronts for doors or drawer fronts.  Cabinets shall meet the ANSI/KCMA A161.1 performance and construction standard for kitchen and vanity cabinets.  Cabinets shall bear the certification seal of KCMA (Kitchen Cabinet Manufacturers Association).

4.	A pantry closet is required in each unit.  The pantry must be 1’6” x 1’6” deep with a minimum five shelves, located in or adjacent to the kitchen.

5.	Fluorescent lighting is required.

Bathroom Spaces:

1.	Tub/shower units should have minimum dimensions of 30-inch width by 60-inch length and be equipped with anti-scald valves.  All tubs in designated handicap accessible units must come complete with “factory-installed grab bars”.

2.	Water closets should be centered 18 inches from sidewalls or vanity/lavatories.

3.	Mirror length should extend to top of vanity backsplash with top of mirror a minimum of 6’-0” above finish floor.  Framed decorative mirrors or medicine cabinets with mirrors are allowed with a minimum size of 14” x 24”.

4.	Vanity cabinets or a medicine cabinet shall be provided in all units.  All cabinets in designated handicap accessible units must be installed at ADA mounting heights.

Hallways should have a minimum width of 36 inches.

All interior doors to habitable spaces should have minimum width of 30 inches.

Overhead lighting is required in each room.

Window treatments are required for all windows.

Sliding glass doors are prohibited.

Floor Finishes:

1.	Carpet materials must meet FHA minimum standards.

2.	Resilient flooring materials must meet FHA minimum standards.

A minimum of two hard-wired with battery back-up smoke detectors is required per unit.

A carbon monoxide detector must be installed in each unit. (Only for projects using gas.)

9.	Plumbing and Mechanical Equipment:

a.	Water heaters should be placed in drain pans with drain piping plumbed to the outside.  Pipe all T&P relief valve discharges direct to exterior of building and elbow down to 6” above finish grade.

b.	Through-wall HVAC units are not permitted except in efficiency units or in offices.

c.	CPVC supply piping is not allowed for interior space in-wall or overhead services.

d.	HVAC refrigeration lines shall be insulated.

e.	HVAC 13 seer or greater should be used.  HVAC equipment should be placed so that their operation does not interfere with the comfort of the adjacent dwellings.

C.	Modular Construction:

1.	Modular units are to be constructed in component sections and assembled by a manufacturer in a controlled environment.  The component sections are to be assembled on a conventional permanent foundation at the project site.  Finish work is to be completed on site.

2.	Modular units must be constructed to meet applicable building codes, AHFA’s specifications and Design Quality Standards stated herein.

- A modular home manufacturer’s warranty must be provided.

III.	Drawing Submission Criteria:

The following documents should be prepared by a registered architect, surveyor, or engineer licensed to practice in the State of Alabama.

A.	Site Plan: The following items should be shown.

1.	Scale: 1 inch = 40 feet or larger for typical units.

2.	North arrow.

3.	Locations of existing buildings, utilities, roadways, parking areas if applicable.

4.	Existing site/zoning restrictions including setbacks, rights of ways, boundary lines, 	wetlands, and flood plain.

5.	All proposed changes and proposed buildings, parking, utilities, and landscaping.

6.	Existing and proposed topography of site.

7.	Finished floor height elevations and all new paving dimensions and elevations.

8.	Identification of all specialty apartment units, including, but not limited to, designated handicapped accessible and sensory impaired apartment units.

9.	Site accessibility design requirements.

B.	Floor Plans:

1.	Scale: 1/4 inch = 1 foot or larger for typical units.

2.	Show room/space layout, identifying each room/space with name and finished space size.

3.	Indicate the total gross square foot size and the net square foot size for each typical unit.

C.	Elevations and sections for new construction:

1.	Scale: 1/8 inch = 1 foot or larger.

2.	Identify all materials to be used on building exteriors and foundations.