Addendum A

2012 Design Quality Standards

(For Attached Rental Units)

The following outline of minimum standards must be used in designing Housing Credit and HOME projects of twelve or more units.

Any deviations from these standards should have the prior written consent or approval of the Alabama Housing Finance Authority fourteen (14) days prior to submitting an application for funding.  Any deviation requested and approved less than fourteen (14) days prior to submitting an application will be charged $500.

Any deviations from these standards after the reservation for funding and through the construction of the project should have the prior written consent or approval of Alabama Housing Finance Authority before the work has commenced.  Any deviation requested and approved will be charged $500.

All projects must be designed in accordance with the applicable requirements of the Americans with Disabilities Act, Section 504 Requirements, Fair Housing and any local building codes.

I.	Site Selection Criteria:

A.	HOME proposed sites containing property within a 100-year flood plain and/or wetlands are not permitted.

B.	Sites located in a Radon Zone-1 (highest level) will require Radon Resistant New Construction Practices.  Rehabilitation projects must meet the Radon Mitigation Standards as required by the Environmental Protection Agency.  The following counties are located in Radon Zone -1:  Calhoun, Clay, Cleburne, Colbert, Coosa, Franklin, Jackson, Jefferson, Lauderdale, Lawrence, Limestone, Madison, Morgan, Shelby, and Talladega.

C.	All new construction developments must submit a complete site specific soils report, not more than one year old at the time of submission of final plans and specifications, bound within the project specifications.  Rehabilitation projects adding any new building foundations must submit a foundation specific soils report.  The soils report must reflect the results of laboratory tests conducted on a minimum of one (1) soil boring per planned building location and a minimum total of two (2) soil borings at the planned paved areas of the development.  A registered professional engineer or a certified testing agency with a current license to practice in the State of Alabama must prepare the report.

D.	Sites located outside municipal city limits:

1.	A proposed new construction site may be located outside a municipality’s city limit, but must be within the local police or sheriff jurisdiction.

2.	A proposed site that is located in the police jurisdiction of a local municipality must comply with applicable zoning restrictions as if located within that municipality’s city limit.

3.	Domestic water and fire water service must be provided to the development by the local utility service provider.

II.	Building Design Criteria

A.	Maximum Building Standards:

1.	The square footage of the Project’s community building must not exceed 2,500 square feet heated and cooled (inclusive of the office area, community laundry, community meeting room, restrooms, kitchens, etc.) and be ADA accessible.

2.	All 100% Elderly projects must be one-story structures.  Exception: Projects may have more than one story, provided elevators are to be installed servicing all upper level apartments.  Design exceptions, or deviations, may be reviewed by AHFA on an individual basis.

B.	Minimum Building Standards:

1.	Minimum Apartment Unit Net Area Requirements:

a.	“Net” area is measured from the interior finished face of the exterior wall to the centerline of the common, or party, wall.

b.	Minimum Bedroom Net Area is measured from the interior faces of all walls surrounding each bedroom, excluding closets, mechanical rooms, and storage rooms.

| Unit Type | Number of Bathrooms | Minimum Unit Net Area* | Min. Bedroom Net Area |
| --- | --- | --- | --- |
| 1 Bedroom | 1 | 725 s.f. | 120 s.f. |
| 2 Bedroom | 1 | 900 s.f. | 120 s.f. |
| 2 Bedroom | 1.5 | 925 s.f. | 120 s.f. |
| 2 Bedroom | 2 | 975 s.f. | 120 s.f. |
| 3 Bedroom | 2 | 1,200 s.f. | 120 s.f. |
| 4 Bedroom | 2 | 1,455 s.f. | 120 s.f. |

*Note 1: Unit areas do not include outside storage, covered porches, patios, balconies, etc.

2.	Exceptions to the minimum area requirements:

a.  Projects with USDA Rural Development (formerly FmHA) financing;

b.  Single-Room Occupancy (“SRO”) projects; and

c.  Rehabilitation of existing residential rental units.

3.	For new construction, all units must include an exterior storage closet with a minimum area of sixteen (16) square feet.

4.	Exterior Building Standards:

a.	Exterior Finishing Materials:

1.	Exterior building coverings: For new construction, very low maintenance materials are required. Acceptable materials include:

a.	Brick;

b.	High quality vinyl siding with a minimum thickness of .042 and a lifetime non-prorated limited warranty (50 year) transferable; or

c.	Cementitious siding.

All siding materials listed above are required to be 8 inches above the finished floor elevation of the building ground floor, with the exception of concrete patio and covered breezeway areas.  Brick or decorative block must be used as an apron material.

2.  	Prefinished fascia and soffit: Vinyl, aluminum, and/or perforated cementitious panels should be used and must contain vents.

3.	Windows frames and sashes are to be constructed of vinyl-clad wood, solid extruded vinyl, fiberglass, or aluminum and all windows are required to have screens.

4.	Materials for entry doors are to be metal-clad wood, fiberglass, or hollow metal construction. “Peepholes” and deadbolt locks are required in entry doors.  Dead bolt locks on entry doors should have “thumb latch” on interior side.  Double keyed dead bolt locks are prohibited.  Minimum clear width of all exterior doors shall be 34 inches.

5.	Roofing materials: Anti-fungal shingles or metal roof with 25-year warranty or better should be used.

6.	Roof gable vents should be made of aluminum or vinyl materials.

7.	All attics shall be vented.

8.	All primary entries should be within a breezeway or have a minimum roof covering of 3-feet deep by 5-feet wide, and should be designed to divert water away from the entry door. Entry pads measuring 4 feet by 4 feet and made of impervious material with a minimum slope of 1/4 inch per foot are required at each exterior entry.

9.	All breezeways must be constructed of concrete floor/decking material.

10. 	Exterior shutters are required on all 100% vinyl siding buildings.

11.	 Stairway components, such as stringers, treads, and risers must be constructed from steel or concrete.  Handrails and pickets must be constructed from steel or aluminum.

12.	Patio and porch/balcony components used as part of the building shall have concrete slabs or decks and must be constructed so that no wood is exposed.  Concealment shall be with materials such as aluminum or vinyl siding or cementitious materials.  Structural wood columns shall be at a minimum 6” x 6 pressure treated columns concealed as noted above properly sized fiberglass, high density urethane or aluminum columns.  Decorative rails and/or guard rail systems used at porches and patios shall be code compliant systems of vinyl, fiberglass or metal.  Wood railings are not allowed.

b.	Other Exterior Standards:

1.	Exterior lighting is required at entry doors.

2.	Address numbers are to be clearly visible.

3.	One and one-half parking spaces per living unit required for family units, one space per unit for elderly units, two parking spaces for single family homes, and two parking spaces for each duplex, unless local code dictates otherwise, and no designated street parking allowed.

4.	Metal flashing or 20 mil polyethylene when used in conjunction with a self-adhering polyethylene laminate flashing, should be installed above all exterior door and window units.

5.	A landscaping plan must be submitted indicating areas to be sodded and landscaped. Landscaping plan(s) must follow any applicable landscape municipal ordinance.  At a minimum, all disturbed areas must be seeded.  One 1 1/2” tree per unit.  Six 1 gallon shrubs per unit.

6.	Concrete curbing is required along all paved areas throughout the development site, including parking areas.  (Valley curbs are not allowed)

7.	Sidewalk access to all parking spaces must be provided.

8.	A project sign including the fair housing logo is required.

9.	A minimum of one enclosed on a minimum of 3 sides trash dumpster or compactor is required.  The trash dumpster/compactor must be ADA accessible.

10.	Continuous asphalt or concrete paved access road must be provided to the entrance of the development.

11.	All parking must be asphalt or concrete.  An asphalt or concrete paving recommendation letter must be provided with the application by a geotechnical engineer.

12.	All sidewalks and walkways must be concrete and at least 36 inches wide.  All amenities should be connected to the dwelling units by a sidewalk or walkway.

13.	Mailboxes, playground and all exterior project amenities must be ADA accessible.

5.  Interior Building and Space Standards:

a.	Wall Framing:

1.	Walls may be framed using metal studs in lieu of wood.

2.	Sound proofing or sound batt insulation is required between the stud framing in party walls. A sound rating of STC 54 is required.

b.	Insulation Requirements:

1.	Exterior wall insulation should have an overall R-11 minimum for the entire wall assembly.

2.	Roof or attic insulation should have an R-30 minimum.

3.	Vapor retarders must be installed if recommended by project architect.

c.	Kitchen spaces:

1.	6 1/2-inch deep double bowl stainless steel sinks are required in each unit.

2.	Each unit must be equipped with a 5 lb. ABC rated dry chemical fire extinguisher readily accessible in the kitchen and mounted to accommodate handicapped accessible height in accessible units.

3.	New cabinets should have dual sidetrack drawers and no laminate or particleboard fronts for doors or drawer fronts.   Cabinets shall meet the ANSI/KCMA A161.1 performance and construction standard for kitchen and vanity cabinets.  Cabinets shall bear the certification seal of KCMA (Kitchen Cabinet Manufacturers Association).

4.	A pantry closet is required in each unit.  The pantry must be 1’6” x 1’6” deep with a minimum five shelves, located in or adjacent to the kitchen.

5.	Fluorescent lighting is required.

d.	Bathroom Spaces:

1.	Tub/shower units should have minimum dimensions of 30-inch width by 60-inch length and be equipped with anti-scald valves.  All tubs in designated handicap accessible units must come complete with “factory-installed grab bars”.

2.	Water closets should be centered 18 inches from sidewalls or vanity/lavatories.

3.	Mirror length should extend to top of vanity backsplash with top of mirror a minimum of 6’-0” above finish floor.  Framed decorative mirrors or medicine cabinets with mirrors are allowed with a minimum size of 14” x 24”.

4.	Vanity cabinets or a medicine cabinet shall be provided in all units.  All cabinets in designated handicap accessible units must be installed at ADA mounting heights.

e.	Hallways should have a minimum width of 36 inches.

f.	All interior doors to habitable spaces should have minimum width of 30 inches.

g.	Overhead lighting is required in each room.

h.	Window treatments are required for all windows.

i.	Sliding glass doors are prohibited.

j.	Floor Finishes:

1.	Carpet materials must meet FHA minimum standards.

2.	Resilient flooring materials must meet FHA minimum standards.

k.	A minimum of two hard-wired with battery back-up smoke detectors is required per unit.  Townhomes must have a minimum of one smoke detector upstairs.

l.	A carbon monoxide detector must be installed in each unit. (Only for projects using gas.)

6.	Plumbing and Mechanical Equipment:

a.	Water heaters should be placed in drain pans with drain piping plumbed to the outside.  Pipe all T&P relief valve discharges direct to exterior of building and elbow down to 6” above finish grade.

b.	Through-wall HVAC units are not permitted in residential units except in efficiency units or in offices.

c.	CPVC supply piping is not allowed for interior space in-wall or overhead services.

d.	HVAC units and water heaters are not permitted in attic spaces. Units must be placed in Mechanical Closets with insulated walls located in the living unit.

e.	HVAC refrigeration lines shall be insulated.

f.	HVAC 13 seer or greater should be used.  On single-family homes the HVAC equipment should be placed so that their operation does not interfere with the comfort of the adjacent dwellings.

C.  Modular Construction:

- Modular units are to be constructed in component sections and assembled by a manufacturer in a controlled environment.  The component sections are to be assembled on a conventional permanent foundation at the project site.  Finish work is to be completed on site.

- Modular units must be constructed to meet applicable building codes, AHFA’s specifications and Design Quality Standards stated herein.

- A modular home manufacturer’s warranty must be provided.

Drawing Submission Criteria:

The following documents should be prepared by a registered architect, surveyor, or engineer licensed to practice in the State of Alabama.

A.	Site Plan: The following items should be shown.

- Scale: 1 inch = 40 feet or larger for typical units.

- North arrow.

- Locations of existing buildings, utilities, roadways, parking areas if applicable.

- Existing site/zoning restrictions including setbacks, rights of ways, boundary lines, wetlands, and flood plain.

- All proposed changes and proposed buildings, parking, utilities, and landscaping.

- Existing and proposed topography of site.

- Finished floor height elevations and all new paving dimensions and elevations.

- Identification of all specialty apartment units, including, but not limited to, designated handicapped accessible and sensory impaired apartment units.

- Site accessibility design requirements.

B.	Floor Plans:

- Scale: 1/4 inch = 1 foot or larger for typical units.

- For projects requiring renovation and/or demolition of existing structures, show proposed changes to building components and design, identifying removal and new construction methods.

- Show room/space layout, identifying each room/space with name and finished space size.

- Indicate the total gross square foot size, and the net square foot size for each typical unit.

- For projects involving removal of asbestos and/or lead paint, identify location and procedures for removal.

C.	Elevations and sections for new construction:

- Scale: 1/8 inch = 1 foot or larger.

- Identify all materials to be used on building exteriors and foundations.